Diff Ratio ID

If you have the axle code of your vehicle, it is easy to find out what size differential, what ratio, and what pinion set-up you have. This will also help if you are hunting for a particular unit off another vehicle. The axle code is in the vehicle ID plate under the hood or drivers door. The axle code is 4 digits: a letter followed by 3 numbers.

Example: F372 = 7.5" 3.58 final ratio 2 pinion

code:--------------------------------------------------------------------------------1ST DIGIT R&P SIZE 2nd/3rd Digit R&P RATIO 4th DIGIT PINION SET-UP

A 	138mm 	O1 	3.30 	2 	2 pinion

B 	145mm 	O2 	3.36 	3 	2 pinion LSD

C 	6.25" 	O3 	3.55 	4 	4 pinion

D 	6.62" 	O4 	3.56 	5 	4 pinion LSD

E 	7.1" 	O5 	3.70

F 	7.5" 	O6 	3.89

G 	8.0" 	O7 	3.90

H 	9.0" 	O8 	4.11

J 	9.25" 	O9 	4.22

K 	9.5" 	10 	4.38

L 	10.5" 	11 	4.44

M 	12.5" 	12 	4.63

N 	13.5" 	13 	4.79

P 	14" 	14 	4.88

R 	162mm 	15 	5.13

S 	6.38" 	16 	5.29

T 	6.7" 	17 	5.60

U 	6" 	18 	5.71

V 	10.6" 	19 	5.83

W 	15.5" 	20 	6.17

X 	142mm 	21 	6.67

Y 	158mm 	22 	6.78

23 	6.83

24 	7.64

25 	4.56

26 	5.57

27 	3.36

28 	4.30

29 	4.10

30 	3.73

31 	3.91

32 	6.59

33 	7.50

34 	6.78

35 	7.64

36 	4.78

37 	3.58

38 	3.42

Tacomas:

The axle code for your rig can be found on the manufacture's sticker located on the driver's side door jamb as follows:               First digit:           A = 7.5" ring gear

B = 8" ring gear

Next two digits: 01 = 3:42

02 = 3:58

03 = 4:10

04 = 4:56

05 = 3:15

06 = 3:91

Last digit:

A = 2 Pinion, Open

B = 4 Pinion, Open

C = 2 Pinion OEM Limited Slip

some '98-00 models have shown a BO code of "???" on the door plate; so far this turns out to be a 3.91 gear ratio.